Kubota outlines the following troubleshooting methods and flow chart for an L2550 with the service complaint: "Tractor Does not Move" (under no load)
Before getting into reading this flow chart make sure your tractor is in fact a GST Model, check identification plate, must say L2550DT-GST.
Type and amount of transmission oil conform to Kubota specification?
If NO-drain and replace with correct fluid
If Yes-check Front End Loader or lower link of 3 Point, does it
rise up correctly?
If NO-clogged Hydraulic Filter or Faulty Hydraulic Pump
If YES-Does Power Steering Operate?
If NO-Faulty Hydraulic Pump on the Power Steering Side
If YES-Measure the pressure at port 5, pressure rise conforms to the
pressure table (P5)?
If YES-Worn clutch pack disc (only work under load) Fault other than
GST system (broken shift fork, worn main clutch etc)
If NO-measure pressure at port 6., pressure rise conforms to the
pressure table P6?
If NO-Prescribed pressure is achieved only on shift position "N"-
Faulty clutch pack sealing
If NO-Prescribed pressure is below the prescribed level in all shifts
"N" to 8th", then measure the pressure of port 7, pressure
rise conforms to the pressure table P7?
If YES-prescribed pressure at port 6 conforms to pressure table P6,
then measure the pressure at port 3. Pressure rise conforms to
pressure table P3?
If NO-prescribed pressure at P7 is below the prescribed pressure
level in all shifts from "N" to 8th"-Fault in the relief valve or
reducing valve
If pressure measured to P3, conforms to the pressure table (P3),
then measure the pressure at port 4 to see if it conforms to the
pressure table for P4
If presure measured at P3 does not conform, Fault in the shuttle
shift spool valve, gate valve, (shuttle gate) or rotary valve
If pressure measured at P4 conforms to the pressure chart for P4,
then measure the pressure at P1, pressure rise coconforms to the
the pressure table for P1?
If pressure measured at P4 does not conform, Fault in Hi-Lo shift
spool valve, gate valve (Hi-Lo gate) or rotary valve
If the pressure measured at P1 conforms to the pressure chart for P1
then measure the pressure at port 2, pressure rise conforms to the
pressure table for P2?
If the pressure measured at P1 does not conform, Fault is in the
3rd to 4th shift spool valve, gate valve (3-4 gate) or rotary valve
If the pressure measured at P2 conforms to the pressure chart for
P2-Fault of Modulating Valve or gate valve
If the pressure measured at P2 does not conform, Fault is 1-2nd
shift spool valve, gate valve (1-2 gate) or rotary valve
This is a long involved process of diagnosis for a GST Kubota that won't move when shifted! I'm winded just typing the procedure out!
However, I think an important piece of your information is "after shutting tractor off it then moves and there is no problem", leading me to think that the hydraulic filter is plugged on your tractor.
Shutting down causes a back flow of residual pressure that clears the blockage at the filter allowing the tractor to move. Here's your homework assignment-hey, it's gonna take some work at your end too!
Dump the trans oil-all 7 and a half gallons of it! There are two hydraulic filters on the L2550GST, one serves the P/Steering circuit, the other the transmission, change them both! Make sure to fill the filters with new oil before spinning them on. Fill the tractors transmission and see if this fixes your problem. If it doesn't, then it needed to be done anyway! Report back and let us know what you find. I have a few ideas if your tractor is a mechanical shuttle shift as well!
__________________